## Slide 1: Municipal Energy Planning
Chris Mason, Northampton Energy & Sustainability Officer
For June 22, 2022 CMRPC Panel

## Slide 2: A Growing Shift in Perspective
Cost-effective Energy Use Reduction
% energy use reduction goals
Simple payback times
Bundled savings pays financing of efficiency improvements
Positive cash flow over long terms
MassSAVE incentives based on avoided costs of new power plants
Meeting Greenhouse Gas (GHG) Reduction Goals
Net-zero GHG emissions
Eliminate on-site use of fossil fuels
MassSAVE has added incentives to support state GHG reduction goals and equitable distribution of incentives
  Stronger incentives for weatherization and electrification
Notes: Over the last 4 to 5 years – from mostly cost-effective goals to including GHG reduction goals

## Slide 3: In Response to Climate Commitments
Northampton’s Climate Commitments
City government buildings and operations to be net carbon neutral by 2030.
To become a net carbon neutral city by 2050.
Massachusetts Climate Goals
50% lower than 1990 baseline by 2030
  GHG emissions from electricity reduced by 95% by 2050
Net zero emissions in aggregate in building sector by 2050.
Notes: In 2018, Mayor Narkewicz committed the City of Northampton
to becoming a net carbon neutral city by 2050. City Council
endorsed this goal in 2018.
CRRP: Ensure that city government buildings and operations are net
carbon neutral by 2030.
“We have to stop replacing steam boilers with new steam boilers”

## Slide 4: We Need a Roadmap How to prepare buildings for when HVAC equipment ages out?
Capital Improvement Funds paying for Technical Studies
  Seven City Facilities (complete)
  Three elementary Schools (on-going)
  Three more schools (FY 2023 budget)
  For these studies:
  Net-zero is defined as no on-site burning of fossil fuels.
  The City is depending on the state to achieve its goal of carbon-free electricity by 2050.
  The City could opt to create (or buy) its own carbon-free electricity sooner
Notes: E.g., the plan is to prepare buildings so that we can replace boilers with non-fossil fuel based heating and cooling equipment when old equipment ages out.
Identify buildings or wings of buildings with greatest GHG reduction potential
Look for opportunities to combine GHG reduction goals with other goals (e.g., educational, facility maintenance)
  Steps
  Building envelope improvements
  Mechanical upgrades
Coldham & Hartman and team completed a study of 7 City buildings in November 2021
Building Cost ($ millions)
Average $1.9M (all-in costs)
Jones Whitsett and team began a study of three elementary schools in December 2021
Preliminary: $6.5M to $8.2M per school

## Slide 5: Basic Process
Evaluate initial conditions
  Building envelope
  HVAC/mechanical systems
  Current energy use & behavior
Construct Energy Models
Identify potential measures to reduce energy use intensity (EUI)
  Assign cost estimates
Identify potential alternative non-fossil fuel based mechanical systems
  Assign cost estimates
Guide city in order of implementation and deciding between alternatives
Notes: EUI reduction decisions involve trade offs
City facilities, aim was for peak heating load to be below 20 BTU/hr-sqft; (the amount of heat that must be added over an hour's time to keep the space warm)
Schools, aim is for an EUI of 35 KBTU/sq-ft (energy per square foot per year)

## Slide 6: Example: Leeds Elementary School
1953 Wing
1991 Addition
VFDs & Updated EMS
RCx pneumatic controls
LED lighting
Melink Kitchen Hood
Low flow water fixtures
Steam trap and radiator valve repairs
Storms added to single-pane windows
Added insulation to many roofs
Work already completed
Notes: Note: 1991 wing heated with steam to hot water exchanger.

## Slide 7: Existing Conditions
1953 Wing
Steam boiler & distribution systems
Unit Ventilators for fresh air
Original windows w/storms added
Poorly insulated & air-sealed attic
Uninsulated brick walls
Uninsulated crawl space
1991 Wing
Hot water heat from steam boiler via heat exchanger
Unit ventilators for fresh air
Double-pane windows
No under-slab insulation
Uninsulated brick walls
Insulation added under new rubber roofs

## Slide 8: Planned Approach
PHASE 1 – 1953 Wing
Step 1 – Envelope Improvements
  Air-seal and insulate attic
  High efficiency windows
  Insulate walls & crawlspace
Step 2 – Mechanical Improvements
  Replace unit ventilators with ERVs
  Install VRF/Heat Pump system
  Decommission steam boiler
PHASE 2 – 1991 Addition
Step 3 –Interim Mechanical Improvements
  Replace steam with high-efficiency gas boiler sized for 1991 wing
  Replace unit ventilators with ERVs
PHASE 3 – 1991 Addition
Step 4 – Envelope Improvements
  Walls, windows
  Comprehensive air-sealing
Step 5 – Mechanical Improvements
  Replace gas boiler with VRF/Heat Pump system
ONSITE GENERATION
PV/Electrical Upgrade
Install onsite PV Array and Upgrade Electrical System Capacity

## Slide 9: Existing & Anticipated Funds
Existing:
  Green Communities Grant :
    Air seal and improve attic insulation
    Design VRF/Heat Pump and ERV systems
  Approved Capital Improvement Funds to design replacement windows
Anticipated:
  Green Communities Grant to implement mechanical improvements
  Capital Improvement Funds to replace windows

## Slide 10: Need to be flexible No Funds to Insulate Walls or Crawl Space?
Size VRF/Heat Pumps for load WITH insulated walls and crawl space
Supplement VRF/Heat Pump system with steam heat until walls and crawl space can be insulated

## Slide 11: Questions?

## Slide 12: 7 City Buildings - Selected Recommendations
Centralized Geothermal System Recommended for City Hall, Memorial Hall, Academy of Music & Municipal Building
  Requires study to identify potential for well field
  Centralized air to water (A2W) heat pump recommended as alternative
  Individual GSHP or A2W systems could be employed to avoid logistical problems with a centralized system
Municipal Building is highly problematic and may be worth replacing
  Consider more efficient use of space in City & Memorial Halls
First in line: City Hall
  To avoid boiler replacement
Low Priority Buildings: Police HQ, Fire HQ and Forbes Library
  Smallest carbon reduction potential
  Newer HVAC systems not yet at end of life
Notes: Pros and cons have not been hashed out and a way forward has not been identified.

## Slide 13: Projected Costs – City Buildings Includes construction, design contingency, overhead & profit, and soft costs
Building | Cost ($ millions)
Memorial Hall | 2.7
Municipal Building | 2.27
City Hall | 2.15
Academy of Music | 2.95
Forbes Library | 1.26
Fire HQ | 0.93
Police HQ | 1.12
Notes: Roughly 10M for four centralized buildings
Roughly 3.3M for later buildings
Costs would be trimmed if we chose A2W

## Slide 14: Projected 30-Year CO2e Reduction Based on expected grid emissions
Building | Tons CO2e - BAU | Tons CO2e - With Improvements | Tons CO2e - Difference
Memorial Hall | 2,360 | 243 | - 2,117
Municipal Building | 3,050 | 258 | -2,792
City Hall | 2,059 | 220 | -1,839
Academy of Music | 4,503 | 499 | -4,004
Forbes Library | 4,255 | 704 | -3,551
Fire HQ | 4,973 | 538 | -4,435
Police HQ | 2,602 | 766 | -1,836

## Slide 15: Current Study - Three Elementary Schools
Switch to PDF file